## Slide 1
forklift
TLILIC0005
Full Training
Licence to operate a

## Slide 2
HOUSEKEEPING
Emergency
evacuation
Toilets
Smoking area
Phones
Duration
and breaks

## Slide 3
Momentum High Risk Training - 3rd party provider
  MyneSight is a registered training organisation (RTO)registered by ASQA to deliver vocational education and training
  (VET) services. MyneSight is responsible for the quality of the training and assessment in compliance with the ASQA
  RTO Standards and the Australian Qualification Framework (AQF) for the issuance of certificates.
  Student Handbook
  The Student Handbook provides all the key information you’ll need to participate in this program including, but not limited to, the following:
Privacy and Confidentiality / Access and Equity
Code of Conduct
Alcohol, Drug and Medication
Training and Assessment
Learning Support
Fees, Charges and Refunds
Issuance of Awards / Complaints and Appeals

## Slide 4
CODE OF CONDUCT
Adhere to all safety requirements
Treat other participants with dignity and respect
Behave at all times in a reasonable manner
Attend and arrive on time to all sessions
Participate willingly and actively in all activities
Comply with the facility/site policies and procedures
Do not use your mobile phone whilst in the practical training yard
Please step out of the classroom if required to take a phone call
Follow trainers' instructions

## Slide 5
Privacy Notice
Under the Data Provision Requirements 2012, MyneSight Pty Ltd is required to collect personal information about you and to disclose that personal information to the National Centre for Vocational Education Research Ltd (NCVER).
NVCER will collect, hold, use and disclose your personal information in accordance with the Privacy Act 1988 (Cth), the National VET Data Policy and all NCVER policies and protocols (including those published on NCVER's website at www.ncver.edu.au).
For more information about NCVER's Privacy Policy go to https://www.ncver.edu.au/privacy
A privacy notice declaration is included on your Registration Form (Section 13).
Registration Process

## Slide 6
If deemed competent you receive an email from WHSQ licensing and a link to apply for your HRWL
You will receive a Statement of Attainment awarded from MyneSight.
1
2
OUTCOMES

## Slide 7
Legislation & Compliance
Safety and Compliance Documents
Workplace Health & Safety Act & Regulations
Codes of Practice 2006 - Mobile Crane
Australian Standards – Lifting equipment; height work; Cranes, hoists and winches
Risk Assessment & Lift Plan documentation
Industry standards and Advisory Standards
All work activities are guided by safety and compliance documentation

## Slide 8
WHAT IS A FORKLIFT
A forklift is a powered industrial truck equipped with a mast and an elevating load carriage to which is attached a pair of fork arms or another attachment.

## Slide 9
TYPES OF FORKLIFTS

## Slide 10
Parts Of A Forklift

## Slide 11
The point of balance (fulcrum) is located at the front axle of the forklift, where the wheel touches the ground
Everything behind the front axle of the forklift is used to counter the weight of the load that is being lifted (counterweight).
Counterbalanced Forklifts
Counterbalanced Forklifts are the most common type

## Slide 12
LICENCING REQUIREMENTS
Once you pass your dogging theory, calculations and practical assessment you have 60 days to apply for your HRWL online.
A HRWL is valid for 5 years. You must renew your licence within 12 months after expiry or it will be cancelled
Can you perform High Risk Work if you do not have a HRWL?
Only if you have been enrolled with an Registered Training Organisation and are supervised by someone with the relevant class of HRWL
If you are no longer competent you must hand your licence back to the regulator or be retrained

## Slide 13
You have a responsibility to give the correct information and paperwork to be completed
Your full name and provide photographic ID
Let your trainer know if you have had your licence refused, suspended or cancelled
You can’t currently hold the HRWL for the course you are attending
Answer everything truthfully
Let the trainer know if you have been found guilty under the WHS laws anywhere in Australia

## Slide 14
PCBU’s/Employer’s duty of care
An employer must provide a workplace that is safe and without risk to health.
An employer must provide instruction, training and supervision for employees to work safely
Employee’s duty of care
An employee must take care of your own health and safety—and the health and safety of other people in the workplace..
Duty of care

## Slide 15
Penalties
Failing to work safely, the WHS Regulator may;
Suspend your HRWL
Cancel your HRWL
Refusing to renew your HRWL
Order you are reassessed to prove competency
Commence legal proceedings

## Slide 16
Evidence of competency
Your employer may ask you for evidence that you are competent to do high risk work;
Show your HRWL – LF
Show your registration form and are in training for the class of HRWL
Show your Candidate Assessment Summery

## Slide 17
Before starting work onsite
You need to talk to/consult with your workmates, supervisors, safety officers, the council, engineers and managers.
What important information would you ask about?
Known hazards and current controls (inc permits)
Site specific workplace rules and procedures
Emergency procedure
Plan Job

## Slide 18
Planning and considerations
Plant and equipment needed for task
Permits
Location of task
Availability of equipment
Communications methods
Entry and exit points
Task plans/drawings
Specifics of task
Weights of loads
Type, capacity of the forklift
Number of people required for the job
Attachments required
Plan Job
There are a number of things to think about when you plan your task.

## Slide 19
Plan Job
You need to plan the path of travel before you start the job
Keeping people out of the path
Do you need a spotter
How will communicate
It is important that you are aware of the requirements relating to your work. Before you begin your tasks ensure that you access the relevant documentation and plan your work.
Check that the forklift will fit and that there are no obstacles in the way. Also check for any other equipment or people working in the area.

## Slide 20
Safe Work Practices
Safe work practices are methods that must be implemented to make sure a job is carried out as safely as possible.
Safe work practices include:
Day to day observation of OHS/WHS policies and procedures.
Emergency procedures.
Risk assessment.
Use of basic fire-fighting equipment
Safe work practices should be referred to, and documented, when completing Safe Work Method Statements/JSA as a guideline for how to carry out a task safely.
General requirements for use of personal protective equipment and clothing.
Smoking in designated areas.
Housekeeping to ensure a clean, tidy and safe work area.
Preventing bullying and harassment.
Storage and removal of debris

## Slide 21
What is a Risk?
Identify workplace hazards
What is a hazard?
A hazard is a thing or situation which can cause injury, harm or damage.
A risk is the likelihood or probability the hazard will cause harm

## Slide 22
HAZARDS
How to look for Hazards at your work place

## Slide 23
WORKPLACE HAZARDS
Overhead cables or power lines
Other traffic (people & mobile machinery)
Buildings and structures
Ground conditions (weather, gradients, soft )
Environmental conditions (wind, rain)
Untrained people
Equipment failure
Enclosed or confined spaces
Forklift tasks present a number of hazards, including but not limited to

## Slide 24
WORKPLACE HAZARDS
Poor communication methods
Transporting dangerous materials
Poor lighting
Load falls
Operating outside of equipment limits
Overloading
Striking other objects or persons
High wind, lightning, heavy rain, dust

## Slide 25
Weather conditions
Storms and heavy rain can cause poor visibility and unstable ground conditions
Stop work, until the rain has cleared.
Recheck the ground conditions
Wind.
Lightning.
Rain

## Slide 26
ELECTRICAL HAZARDS
Working near powerlines can be very dangerous.
The operator is required to know the safe operating distances for different voltages of powerlines. The operator should call the power provider.
In Queensland
POWERLINE VOLTAGES | SAFE DISTANCE
Up to 132KV | 3m
132KV up to 330KV | 6m
330KV up to 500KV | 8m
If you need to work closer than these stated distances you must;
Contact the power company
Have the powerlines insulated
Use an authorised electrical spotter
Have the powerlines shutdown/isolated

## Slide 27
ELECTRICAL HAZARDS
What are some visual indicators or warning that powerlines are near?
HAZARDS
Tiger tail are black and yellow tubes that clip onto powerline
Signage
Powerline markers

## Slide 28
Flammable atmospheres and handling flammable materials
Safe work practices are also vital when fuelling forklift trucks or charging batteries.
Potential ignition sources include:
flames or sparks from an exhaust
heat generated by the engine or exhaust
flashback produced by vapours being drawn into the engine
over-revving the engine
excess speeding
sparks and heat generated by brake components
sparks from tynes striking concrete
static electricity discharged by tyres rubbing up against something
an arc from a starter motor or electrical equipment.

## Slide 29
If you store or handle flammable dangerous goods, you should:
review the MSDS and package labelling to identify the hazardous properties of each flammable dangerous goods
classify areas within the workplace where flammable liquids, gases or solids are stored or handled as hazardous areas according to AS/NZS 60079.10.1:2009 Explosive atmospheres – Classification of areas – Explosive gas atmospheres (IEC 60079-10-1, Ed.1.0(2008) MOD)
identify each hazardous area with markings, warning lights and warning signs
separate ignition sources from hazardous areas by an appropriate distance or physical barriers
provide training and supervision to workers about the risk of ignition sources and how to prevent fire or explosion
never use a spark ignition, forklift truck (including petrol and LP gas-powered) in any hazardous area
Hazardous areas

## Slide 30
Confined spaces
Exhaust emissions from forklift trucks operating in confined spaces can lead to carbon monoxide poisoning.
Carbon monoxide is an odourless, colourless and poisonous gas. Precautions must be taken when forklift trucks are used in confined spaces such as cold rooms and freezers to ensure exposure to toxic levels are kept as low as possible
If using a combustion engine forklift in confined space your should-
Use electric forklift trucks instead of fuel or LP gas-powered types
Monitor and record carbon monoxide levels around workers. Personal or area monitoring can be undertaken.
Confined spaces

## Slide 31
Safe Work Method Statements
A Safe Work Method Statement (SWMS) details how specific hazards and risks, related to the task being completed, will be managed and is developed by the employer/PCBU for their employees/workers.
SWMS fulfill a number of objectives:
They outline a safe method of work for a specific job.
They provide an induction document that workers must read and understand before starting the job.
They assist in meeting legal responsibilities for the risk management process, hazard identification, risk assessment and risk control.
They assist in effectively coordinating the work, the materials required, the time required and the people involved to achieve a safe and efficient outcome.
They are a quality assurance tool.
1 | Break the job down into logical steps taking into consideration what is required to be achieved by the task.
2 | Against each step, identify the workplace hazards in this activity i.e. the ways that a person [or plant] could be injured or harmed [or damaged] during each step.
3 | Decide on measures required to mitigate hazards. i.e. what could be done to make the job safer and prevent the injuries or harm that may occur.
4 | Identify roles and responsibilities for actions and outcomes to make ensure risk controls are carried out and supervision of the process occurs.
5 | Ensure the SWMS is fully understood by all workers prior to commencing the task.
Completing a SWMS:

## Slide 32
Risk assessment
Risk controls should be applied before you begin the job and any time a hazard arises.

## Slide 33
Risk assessment
You can utilise a risk matrix to help you score or rate the likelihood and consequence
of the task
Implement control measures to lower the risk

## Slide 34
Barricading
Exclusion zones
Flashing lights
Spotters
Signage
Adequate lights
Demarcation
PPE
Risk controls
Some common risk control measures in forklift operations are;

## Slide 35
Personnel Protective equipment (ppe)
PPE can help reduce the effects or the chance of being hurt, however it is the last line of defence
Persons should confirm PPE requirements, as it may differ depending on the workplace
Safety helmet
Safety glasses
Safety boots
Gloves
Hearing protection
Dust masks
High visibility clothing
Sunscreen

## Slide 36
The Forklift operator is responsible for determining the load weight
Assess the load
Determine the weight of the load
Assess the dimensions of the load
Assess and determine the center of gravity of the load
Check for lifting points
(if using a jib)
Stamped on load
Consignment notes
Weighbridge cert
Weigh the load
Calculate the load
Height & Length
Material of load
Static or dynamic
Measure or Calculate
Identify COG symbol
Manufactures specs
Manufactures specs
Visually inspect
Check for SWL
Engineers' drawings

## Slide 37
Rear End Swing
Rear end swing is the rapid sideways movement at the rear of the forklift truck. This creates a hazard, particularly for pedestrians, other vehicles and structure nearby.
As forklifts steer with the back wheels, the rear of the forklift turns up to three and a half times faster than the front .

## Slide 38
Forklift Stability & Centre Of Gravity
Stability is an important part in the safe operation of forklifts. Some factors that affect the stability or the forklift are:
Centre of gravity.
Height of load when travlling
Load centre distance.
Forklift rated capacity.
Terrane, sloping ground, bumpy, slippery

## Slide 39
These dynamic forces are caused by things like acceleration, braking, operating on uneven surfaces or on an incline, and turning.
The stability, of the loaded truck is affected by a number of e centre of gravity, factors including size, weight, shape, and position of the load. Other factors are the height to which the load is elevated, the amount of forward or backward tilt, tyre pressure, and the dynamic forces created when the truck is moving.
Forklift Stability & Centre Of Gravity

## Slide 40
Forklift Stability & Centre Of Gravity
The centre of gravity of the forklift can move outside the stability triangle if:
The load is picked up on the tip of the forks.
The load is tilted forward.
The load is tilted too far back when raised.
The load is wide.
Forklift movement causes the centre of gravity to shift.

## Slide 41
Load Centre Distance
The distance from the front face of the forks (or the load face of an attachment) to the centre gravity of the load and from the top face of the fork blades vertically upwards is called the Load Centre Distance.
As load centre distance increases, the forklift’s capacity decreases.

## Slide 42
Load Centre Distance
The forklift trucks shown here are rated at 4200kg at 600mm load centre:
Of these forklifts, only forklift B has a load that is within the rated capacity of the forklift:
The load centre distance for forklift B is 500mm (within the 600mm limit for 4200kg). Forklifts A and C have a load centre distance of 700mm and 650mm (beyond the 600mm limit).

## Slide 43
Forklift Rated Capacity
The rated capacity is the maximum load the forklift truck can handle at a specific configuration based on load weight, height and load centre distance

## Slide 44
Forklift Attachments
Before using any attachment on the forklift, make sure you check the manufacturer’s specifications and load chart to see that the attachment can be used safely. Also make sure the attachment is secured properly before trying to lift a load with it.
Rotating Attachment
Drum Clamp
Carpet Spike
Work Platform/Basket
Fork Extensions
Bale Clamp
If you are not familiar with the attachment, read the manufacturer’s instructions and ask a competent person to show you how to use it

## Slide 45
Communications
As a forklift driver you need to be able to communicate with those around you while you work, and you need to be able to understand the instructions to use the forklift safely.
Verbal and non-verbal language.
Written instructions.
Signage.
Hand signals.
Listening.
Questioning to confirm understanding, and appropriate worksite protocol.

## Slide 46
Jib Attachments
The jib attachment should have the Safe Working Load (SWL) marked at every hook position.
The hook on the jib attachment should be able to swivel (not a fixed hook).
Always make sure the jib attachment hook is centred directly over the load before lifting it to prevent the load from swinging on lift and to maintain the forklift’s stability
.
Whenever using a jib attachment make sure you:
Slings and lifting gear need to be inspected before you use them in accordance with AS 1666.1

## Slide 47
Visual & Pre-Start Checks
Before you use the forklift you MUST check that it is safe to use.
Report any problems that you find by tagging out the forklift, Remove the key, report to the supervisor, fill out the logbook
Walk around the forklift and check to see if there is any visible damage. Ensure that you check:
The condition of the forks/tynes or attachment.
Under the forklift for oil leaks.
The condition of the mast and of the hydraulic rams and hoses.
The condition and security of the load backrest (load guard). This is important as the load guard stops the load from fouling the mast and also stops the load from falling on the operator.
For visual evidence of structural weaknesses (including paint separation or stressed welds).

## Slide 48
Visual & Pre-Start Checks
Check the following fluid levels:
Hydraulic oil.
Engine oil.
Transmission oil.
Brake fluid.
Coolant/water.
Fuel.
Battery electrolyte level (if applicable).
Fluid Checks
If you need to refuel the forklift, make sure the engine is switched off. Re-fuelling while the engine is running may cause the fuel to ignite

## Slide 49
Decals And Signage
Check that the forklift has the appropriate signage and labels. This includes the data plate. Make sure you can read it clearly and that it is firmly attached to the forklift.
DO NOT USE A FORKLIFT WITHOUT A DATA/LOAD PLATE!
If the forklift does not have a data/load plate, or you cannot read it, you must tag out the forklift and report the defect to an authorised person.

## Slide 50
Forklift Controls
Check that you can find and identify the forklift controls. Check the operator’s manual if you are unsure.

## Slide 51
Safety Devices
Check that the forklift has the appropriate safety devices fitted. These can include:
Flashing amber light.
Head lights.
Brake lights.
Reverse lights.
Guards:
Roll-Over Protection (ROP).
Falling Object Protection (FOP).
Load backrest.
Foot guard
Horn
3m metre blue light (if fitted)

## Slide 52
Tyres
Check that the pressure of air-filled tyres is correct. This will help to maintain stability for the forklift.
If the forklift is fitted with solid rubber tyres, check that there are no large pieces of rubber missing, make sure that any wear is even between the tyres and make sure that the wear has now reached the wear limit line.

## Slide 53
Forklift logbook
Check for any previous faults with the forklift. Make sure these faults have been fixed before using the forklift.
Three parts to the logbook
Pre – start inspection
Fault recording
Annual inspection

## Slide 54
Start The Forklift
Once you have visually checked the forklift, start it as per the manufacturer’s guidelines
Ensure the park brake is applied
Secure your seatbelt
Turn the ignition key to activate the electrical system
Turn the ignition key to ‘start’ position to start the engine
Release the key once the engine starts
After starting the engine, check all functions of the Forklift including;
  Check the monitoring system and observe all gauges, warning and service lights
  Test the steering and brake controls
  Test the hydraulic controls
  Monitor for any abnormal noises, smells or vibrations
To enter and exit a forklift, use 3 points of contact and do not use the steering wheel

## Slide 55
Forward and Side stability
Conditions that may cause a forklift truck to tip over sideways (lateral instability) include:
Unevenly distributed load.
Turning at an unsafe speed.
Side shift not centred.
Driving over uneven surfaces.
Driving with a flat or underinflated tyre.
Driving too fast (loaded or unloaded).
Turning with the load raised.
Driving with the load in the elevated position.
Operating on a sloping surface.

## Slide 56
LONGITUDINAL INSTABILITY
Conditions that may cause a forklift truck to tip forward lengthways (longitudinal instability) include:
Driving with the load in the elevated position.
Overloading.
Severe braking.
Incorrect use of the mast tilt (especially with the load carried at a high level).
Unevenly distributed load.
Shifting of the load centre forward (centre of load is forward of the approved load centre).
Operating on sloping surface.
Driving over uneven surfaces.
Load not positioned against the heel of the fork arms.
Driving too fast (loaded or unloaded), including reversing
Forward and Side stability

## Slide 57
Stacking loads
You may need to lean out slightly to one side for a better view of the load.
If refilling stock into racking or shelves, you need to make sure that:
Loads are stacked on a firm level site.
Heavy goods are placed at the bottom.
The stack does not become unstable due to height

## Slide 58
Keep the load at about axle height while travelling and tilt the mast backwards for stability.
Do not travel or turn the forklift with the load raised up in the air. The load height can affect the stability of the forklift while travelling, braking or turning. This creates a hazard that could result in the forklift tipping over, rolling over or losing the load.
If the load blocks your view, travel in reverse. Get somebody to direct you and keep an eye out for other people or equipment in the area.
Make sure the warning devices are working correctly and always check your mirrors and look over both shoulders before reversing in the forklift.
Be aware of rear end swing. This can be very dangerous for people nearby.
TRAVELLING WITH A LOAD

## Slide 59
Inclines and declines
• Keep the forks approximately 20-30cm above the ground • Select a low gear when traveling uphill or downhill • When travelling downhill, use the braking force of the engine and the brake pedal to control speed • If the engine stops when the machine is on a slope, depress the brake pedal, lower the fork tynes, apply the parking brake • Do not venture closer than 3 metres to the drop of a bench, consider the Forklifts weight
When travelling on a ramp, ensure that you do not turn on it or travel across it – always be sure to travel up or down.
Turning or travelling across a ramp can affect the stability of the forklift, increasing the chance of tipping or rolling the forklift over.

## Slide 60
Loading docks
You need to constantly monitor the load movement to ensure that personnel/workers in the area are safe, and that the load and forklift are stable.
If loading onto a truck from a loading dock, make sure there are secured dock plates or bridge plates in place
Safe Forklift Operating Procedures
Always operate the forklift truck in adherence to safe operating procedures. These may include:
Reducing speed, avoid using ramps or other inclined pathways, proceeding with caution and being aware of ground and weather conditions (e.g. wet or slippery surfaces).
Using your horn when approaching blind corners.
Always staying in forklift zones and barricading off the work area if there are people nearby.

## Slide 61
FORKLIFTS & PEDESTRIANS
At any time forklifts are being used in an area with pedestrian access, there should always be signs, barriers and designated pedestrian walkways. In public areas a flagman must be used to direct traffic and warn people nearby that there is a forklift being used.
All forklifts should be fitted with safety flashing amber lights and horns.
Barriers with appropriate safety signs, or a traffic controller, should always be provided when the forklift is being operated over a roadway, footpath or public access area.
NEVER lift loads over people’s heads as there is a risk of injury or death if the load or part of the load falls from the forklift truck.
NEVER let people ride or be lifted on the forks or a pallet! Passengers may only be carried on the forklift if it has been designed and equipped to carry more than one person.

## Slide 62
PICKING UP A LOAD
When picking up a load with the forklift ensure that you:
Approach the load from front on.
Insert the forks all the way into the pallet.
Raise the forks and tilt the load back slightly for stability.
Position the load at axle height or as low to the operating surface as practicable for safe travel.
DO NOT carry the load on only one fork arm. If you do the stability of the forklift may be affected, and you may cause damage to the forklift.

## Slide 63
Loading Trucks

## Slide 64
Platform Attachment
The operator shall check that the platform is secured
The operator shall remain at the controls at all times
The operator shall watch for overhead obstructions
Forklift Work Platforms
Use a platform that is rated not a pallet
Forklift should not carry personnel unless it in accordance with the AS 2359.1
Personnel/workers must remain in the work platform during raising or lowering and must not be moved from place to place other than for small positional adjustments

## Slide 65
Emergency Procedures
If something goes wrong while you are using the forklift it is important that you have an idea of what to do.
In the case of any workplace emergency you must make sure that you:
Alert the relevant personnel/workers of the emergency situation.
Communicate the nature of the emergency to the supervisor and others.
Inform personnel/workers of unsafe areas.
Provide information to emergency services

## Slide 66
If you lose control of the forklift and it begins to tip sideways:
Remain in the forklift.
Brace yourself until the forklift is stationary and is safe to exit.
DO NOT try to jump from the forklift while it is tipping over.
FORKLIFT ROLLOVER PROCEDURE

## Slide 67
ELECTRICAL HAZARDS
In the event of a forklift truck contacting a powerline, the operator should:
Warn others to stay away
Raise the emergency/alarm
If practical, try to break contact with powerline
wait until the powerline power is shut off before leaving the forklift
If the forklift has become unsafe (fire etc..) jump well clear of forklift, Do Not touch the forklift and the ground at the same time
Hop of shuffle away at least 8m meters
Make sure the area is safe and the powerlines have been isolated
Tagout forklift and it must be fully inspected competent person before use

## Slide 68
If the load drops suddenly, or you suspect there is a problem with the hydraulic system, immediately lower the load and turn off the forklift.
Check the forklift for any signs of damage or wear and check hydraulic lines for splits or bulges. Report the fault to an authorised person.
Forklift Malfunction

## Slide 69
Shut Down And Secure Forklift Truck
When you have finished using the forklift, you need to park it, remove the keys and conduct post-operational checks
Always park the forklift on a flat surface out of the way of other traffic.
DO NOT park the forklift:
On sloping surfaces.
Near First Aid stations.
Near fire-fighting appliances.
Near doorways.
On or near pedestrian walkways.
Emergency exits.
Where it is obstructing other traffic.
Next to train tracks (no closer than 2m).
Under overhead electric/power lines where the clearance is insufficient to be safe

## Slide 70
When parking the forklift, normal parking procedures are:
Make sure the fork arms are correctly positioned (tips down, tilted forward, lowered to ground).
Select an appropriate transmission/gear (neutral) and apply the hand/parking brake.
Turn the engine off and remove the keys from the ignition to prevent unauthorised movement of the forklift (if applicable).
Shut off the LPG gas cylinder valve (if applicable).
Any other site-specific procedures as required.
If you have to park the forklift on an incline, make sure you also chock the front wheels in addition to normal parking procedures
If you have to park the forklift on an incline, make sure you also chock the front wheels in addition to normal parking procedures.

## Slide 71
Post-Operational Checks
After you have finished using the forklift, you need to check it to make sure it is ready for the next operator.
Attach batteries to a charger if applicable.
Do not smoke around a charging battery – the fumes could ignite, causing an explosion or a fire.
Always charge batteries in a well-ventilated area away from any naked flame
If you find any fault with the forklift during the inspection:
Stop any operation.
Tag the forklift – put a danger tag on the forklift to stop anybody using it.
Record the problem in the logbook or on the inspection checklist. Give as much detail as possible.
Report the fault to an authorised person.
You may make minor repairs to the forklift if you are competent and authorised to do so

## Slide 72
Keep the batteries charged
Recharge only in a designated well ventilated area
Remove all naked flames within 10m
Keep clear of the battery electrodes
Use suitable personal protective equipment such as gloves, eye shields
Be cautious of the battery weight where movement is required
Ensure battery is secured prior to use
Electric Forklift - Batteries

## Slide 73
1.3.6 REPORTING AND RECORD KEEPING
Make sure you record any action you’ve taken and talk to your supervisor and OHS/WHS officer about the control strategies in place.
Reports and records could include:
Risk Assessment Reports.
Incident Reports.
Job Safety Analysis (JSA).
Safe Work Method Statements (SWMS).
Keeping records is important as they can help ensure that any risk management activities are traceable.
Records also provide a basis for improving methods and tools in the risk management process, as well as improving the overall process.